TECHNICAL NOTES ON ARCSGML 1.0

NOTE: ISO 8879 (Standard Generalized Markup Language) is
      required reading for anyone attempting to implement an SGML
      application.  Its complete official text, incorporating
      the 1988 amendment, extensively annotated and cross-referenced
      and with additional tutorial material, can be found in my
      book, The SGML Handbook, published by Oxford University
      Press, ISBN 0-19-85373-9.  It is available at bookstores and
      through the SGML Users' Group.

A. Compilation and Such

                     All Characters are Unsigned

Work on ARCSGML began in 1983, at the dawn of PC C compiler
technology, so a number of compilers have been used over the years.
As a result, some occurrences of the "char" type are coded with the
typedef "UNCH", which stands for "unsigned character".  As compilers
came along that offered compile-time switches to make all "chars"
unsigned, I stopped using "UNCH" in places.  The bottom line is that
all chars must be unsigned -- how you accomplish it depends on your
coding style and the facilities of your compiler.

                           Non-DOS SGML I/O

NDSGMLIO.SRC is a version of SGMLIO.C with alternative encodings for
other compilers and operating systems.  They are chosen by defining
the following preprocessor names:

TURBOC    Borland C++ 2.0  (same code as in SGMLIO.C)
MICROC    Microsoft C 5.1
IBMC      IBM C for mainframes (not tested)
C88       DeSmet C88 (not tested recently)

SGMLIO.C uses a Borland-specific DOS-specific function called
"searchpath".  Some alternatives for other environments can be found
in NDSGMLIO.SRC.

When NDSGMLIO.SRC is consulted, NDENVCB.SRC will also be of interest.

                                 Lint

Conventional comments for lint are for PC-Lint 2.11 by Gimpel
Software.  However, lint was not run for the SGMLUG original
distribution (ARCSGML 1.0) because Borland C appears to provide
sufficient checking.

Borland C was run with ALL warnings enabled, which required lots of
explicit type casting.  No warnings or errors were issued.

B. Sample Applications ("Text Processors")

The sample text processor that performs markup validation is called
VM2.C or VM2.EXE.  If invoked with the /S option, it will print an
excruciatingly detailed report of the parsing process (see VM2HELP.DOC
for details).  This text processor is used for testing the internal
functions of the parser, so it needs access to "non-ESIS" information
not provided through the usual API.  As such, it is a poor model for
normal text processors, which access the parser control block data
through a friendlier interface provided by SGMLAPI.C.  (See
ARCSGML.DOC for details of the program architecture.)

The sample text processor called APIMODEL is a better model (although
presently untested), as it uses only the normal interfaces of SGMLAPI.
It reads an SGML document and produces a slightly reformatted version.
Although it is not complete, it is easy to see how to use it as a
model for other "translation" applications, such as SGML to a word
processor file.

C. System Declaration Information

A parser constructed with ARCSGML, when used in a conforming SGML
system on an ASCII machine (e.g., PC or PS2), should be capable of
conforming to the following system declaration:

                  SYSTEM "ISO 8879:1986"
                          CHARSET
BASESET  "ISO 646:1983//CHARSET
          International Reference Version (IRV)//ESC 2/5 4/0"
DESCSET  0 128 0

CAPACITY PUBLIC "ISO 8879:1986//CAPACITY Reference//EN"
SCOPE    DOCUMENT
SYNTAX   PUBLIC "ISO 8879:1986//SYNTAX Reference//EN"

                         FEATURES
MINIMIZE DATATAG NO  OMITTAG  YES  RANK     NO  SHORTTAG YES
LINK     SIMPLE  NO  IMPLICIT NO   EXPLICIT NO
OTHER    CONCUR  NO  SUBDOC   NO   FORMAL   YES

                         VALIDATE GENERAL YES
MODEL    NO   EXCLUDE  YES  CAPACITY YES
NONSGML  YES  SGML     NO   FORMAL   YES

D. Interface Specification Notes

The function calls from the text processor to the parser are documented
in SGMLAPI.H.  That file also describes the C structures with which the
API returns information from the parser.  Other parser control blocks 
(with which the text processor normally need not be concerned) are
documented in the other header files.  The following notes supplement the
information in SGMLAPI.H:

   1. Attribute values and SDATA
      entities could contain delimited processing instructions.
   2. Attribute values and CDATA, SDATA, and PI entities could contain
      non-SGML characters (as can content data, described below).
   3. Inline processing instructions are not parsed (except for PIC),
      so character references are not recognized, and non-SGML characters
      cannot occur validly (i.e., through character references).
   4. There are three internal delimiters
      that SGML will insert into returned data:
      tpsw.delcdata brackets a CDATA entity returned in an
                    attribute value.
      tpsw.delsdata brackets an SDATA entity so returned.
      tpsw.delnonch precedes a non-SGML character (see below).
      In addition, an offset,
      tpsw.addnonch, is added to a non-SGML character (modulo 256).
      The delimiters and offset are set in the switch structure; they must
      be non-SGML characters other than 0 8 9 10 13 26 and 28.
      (29, 30, and 31 are the recommended delimiters; 64 us the offset.)
      The CDATA and SDATA brackets can be removed when the data
      is to be formatted.
      The NONCHAR prefix might be needed until the last moment
      for those NONCHARs that have special meaning to a text
      processor, so tpsw.delnonch should be chosen accordingly.
   5. When the recommended delimiters and offset are in use,
      non-SGML characters will be returned as 31,char+64 (modulo 256).
      For example: decimal 22 will be returned as decimal 31, followed
      by decimal 86; decimal 255 as 31 63.
   6. SGML returns resolved notation identifier with NOTATION attribute as
      ADDATA(n).  It is a pointer to a NOTATION control block (see below).
   7. When a start-tag is returned, IDREFL(n) is 1 if the corresponding IDREF
      token refers to an existing ID; it is 0 if the ID hasn't been defined.
   8. When parser returns a start-tag with attributes, an attribute that
      must always be a single token is treated as CDATA, as distinguished
      from a list that just happens to be one token long.
   9. PUBLIC identifier is passed to SGMLIO in ipbfile.ipbp1
      when resolving external identifiers for entities and data content
      notations (programs that access non-SGML data entities).
   10.For RCBDAF returns: if NDESW is on, data ptr is to NDATA entity
      control block.  For AENTITY attributes, ADDATA(i) points to NDATA
      ecb.  The NDATA ecb (struct ne in ADL.H) in turn points to a NOTATION
      control block (struct dcncb in ENTITY.H).  There is code in VM2.C
      that shows how to handle these control blocks.  (You can imbed
      image and graphic entities anywhere that a character entity could
      be referenced.)
   11.You can support device-dependent versions of
      PUBLIC entities (e.g., non-keyable graphic characters), according
      to the syntax of formal public identifiers as defined by the Standard.
      The parser indicates in the FILENAME ipb four entity type codes
      for when a public identifier is versionless and the best available
      version should be substituted.  SGMLIO must find the
      best available version.  (See SGMLCB.H and SGMLIO.C for details.)
   12.If the document element terminates other than by its own end-tag
      or by the end of the document entity, an error message (89) is issued
      and the parser returns an EOD rcb.  Any remaining text in the
      primary entity is ignored.
   13.Multiple passes are supported.  The
      ptrs to rc and rcb in the text processor are passed in
      the switches structure, whose address is sent to the parser
      in the SGMLSET ipb.  At the
      end of the run, SGMLEND must be sent to allow final
      cleanup by the parser.  (See VM2.C for the details.)
   14.SGML keeps a buffer only for the current file.  SGMLIO saves and
      restores the location when a nested file is opened.
   15.Stack of positions (source control blocks) is returned when an error
      occurs, so full entity trace can be printed in error messages.
   16.Trailing RE RS suppression and leading RS insertion for external entities
      set by user parameter (overridable in system ID of ENTITY declaration).

E. Debugging Aids

VM2, because it reveals the internal state of the parser, can be a
useful debugging aid when the /S option is enabled.  In addition, the
TRACESET module contains routines to format and print the parser's
internal control blocks, and to display a vertical "tape" of the
characters parsed and the state transitions they caused.

The various traces are enabled by setting environment variables to an
arbitrary value so that the variables will exist (e.g., SET T=1).
There are separate variables for the prolog (for debugging the DTD
parsing) and the document instance.  They are:

  Prolog         Instance
    PT               T                  trace state transitions
    PA               A                  trace attribute activity
                     C                  trace context checking
    PD               D                  trace declaration parsing
    PE               E                  trace entity activity
    PG               G                  trace group creations
                     I                  trace ID activity
    PM               M                  trace MS activity
    PN               N                  trace notation activity